## Slide 1: Body Drums
Michelle Qiu
Germain Martinez
Gerzain Mata

## Slide 2: Premise
Make the human body the input to the music game.
The microphone is the main input
Output cool graphics
Claps, Snaps, and stomps can be possible inputs

## Slide 3: Block Diagram

## Slide 4: Memory Encoder
Take in memory sequences (parts of song notes)
Compare against input from microphone
OPTIONAL – Take in video images to Graphics module
Take in input from Game FSM for predefined/ custom mode
Take in input from Game FSM for START SONG signal
SONG DONE signal goes high when music is done.

## Slide 5: Audio Module
Take input from MICROPHONE and filter low, mid, and high frequencies
Compare frequencies against note encoding and determine if HIT or MISS
Output result to Game FSM
Most complex part of project

## Slide 6: Graphics Module
Take in graphics from the memory
Output sprites onto the screen and make them fall
When the note hits the Judgement Line then the player has to hit said note.
The line should change color to GREEN or RED to indicate SUCCESS/HIT or FAILURE/MISS
OPTIONAL – Keep a score tally for the player

## Slide 7: Game FSM
Game Logic happens here
In charge of coordinating between modules
Each team member should implement part of the game FSM most pertinent to their individual module

## Slide 8: Specifics
Color
  8-bit color encoding – 256 possible colors
  Use a lookup table  256 x 24 bit lookup table
Notes
  Each note should be 4 bits
  1 note every ½ second  2 notes per second
  8 bits every second  1 byte per second  180 bytes in 3-minute song
Images
  256x256 images
  ~10 total sprites  10 images in memory

## Slide 9: Specifics Cont’d
Images
  256x256x8 bit encoding x 10 images = 640 bytes for image memory