## Slide 1: Real-Time Sound Analysis / Synthesis
Michelle Qiu
Germain Martinez
Gerzain Mata

## Slide 2: Overview
The user sings/ hums/ plays an instrument
A microphone picks up the sound
The sound is saved onto memory for later playback
Audio effects can be added to the sound samples
Two audio samples can be recorded

## Slide 3: Block Diagram

## Slide 4: Memory Handler – Block Diagram

## Slide 5: Memory Handler
Take in input from microphone
Write audio samples to memory
Retrieve sound samples from memory
Retrieve image data from memory for Graphics Module
Bus Sharing – Image and Audio share memory bus
Use ZBT Memory – two 512k x 36 bit memory bus

## Slide 6: Audio Module - Block Diagram

## Slide 7: Audio Module
Take input from MICROPHONE and write to memory
Take EFFECTS from FSM and apply them to recorded audio
Output FFT data to Graphics module
Output sound to SPEAKER
Most complex part of project

## Slide 8: Proposed Effects
Compression & Limiting
Delay & Echo
Expansion & Noise Gate
Phasing
Chorus (if time allows)

## Slide 9: Graphics Module – Block Diagram

## Slide 10: Graphics Module
Take in graphics from memory
Output FFT spectral data
Display running statistics (predominant frequency, amplitude, sample characteristics)
Take in data from ZBT memory
36 bit bus  6 bit pixel encoding = 6 pixels per memory read
6 bit pixel encoding -> 24 bit color to VGA -> LUT
30+ different images for text/numbers/etc.

## Slide 11: Central FSM
Coordinates the modules
Each team member implements part of the FSM most pertinent to their individual module
Choose which bank to record to and what effects to apply

## Slide 12: Specific Number Figures
24 kHz sampling rate and 12 bit encoding scheme
288 kilobits per second data rate
~80 kSlots of ZBT memory required for 10-second recording
Use one bank of memory for each sound recording
Necessary to leave space for image data

## Slide 13: Task Timeline

## Slide 14: Forseeable Challenges
Sharing memory between audio and graphics
Getting FFT statistics in real-time
Simultaneous and offset playback of different recordings